DHT22 manual

1. Connect dht22 module to board:
Pin 1(+3.3V Power) → VCC
Pin 7(PA6) → DC
Pin 9(Ground) → GND
2.Install WiringOP library following next commands:
git clone https://github.com/zhaolei/WiringOP.git -b h3
cd WiringOP
./build

3.Create dht22.c file containing next code:
#include <wiringPi.h>
#include <stdio.h>
#include <stdlib.h>
#include <stdint.h>

#define MAX_TIMINGS 85
#define DHT_PIN 7
int data[5] = { 0, 0, 0, 0, 0 };

void read_dht_data()
{
    uint8_t laststate = HIGH;
    uint8_t counter = 0;
    uint8_t j = 0, i;

    data[0] = data[1] = data[2] = data[3] = data[4] = 0;

    /* pull pin down for 18 milliseconds */
    pinMode( DHT_PIN, OUTPUT );
    digitalWrite( DHT_PIN, LOW );
    delay( 18 );

    /* prepare to read the pin */
    pinMode( DHT_PIN, INPUT );

    /* detect change and read data */
    for ( i = 0; i < MAX_TIMINGS; i++ )
    {
        counter = 0;
        while ( digitalRead( DHT_PIN ) == laststate )
        {
        counter++;
        delayMicroseconds( 1 );
        if ( counter == 255 )
        {
        break;
        }
        }
        laststate = digitalRead( DHT_PIN );

        if ( counter == 255 )
        break;

        /* ignore first 3 transitions */
        if ( (i >= 4) && (i % 2 == 0) )
        {
        /* shove each bit into the storage bytes */
        data[j / 8] <<= 1;
        if ( counter > 16 )
        data[j / 8] |= 1;
        j++;
        }
    }

    /*
     * check we read 40 bits (8bit x 5 ) + verify checksum in the last byte
     * print it out if data is good
     */

    if ( (j >= 40) &&
        (data[4] == ( (data[0] + data[1] + data[2] + data[3]) & 0xFF) ) )
    {
        float h = (float)((data[0] << 8) + data[1]) / 10;
        if ( h > 100 )
        {
        h = data[0]; // for DHT11
        }
        float c = (float)(((data[2] & 0x7F) << 8) + data[3]) / 10;
        if ( c > 125 )
        {
        c = data[2]; // for DHT11
        }
        if ( data[2] & 0x80 )
        {
        c = -c;
        }
        float f = c * 1.8f + 32;
        printf( "Humidity = %.1f %% Temperature = %.1f *C (%.1f *F)\n", h, c, f );
    }
    else {
       printf( "Data not good, skip\n" );
    }
}

int main( void )
{
    printf( "DHT22 temperature/humidity test\n" );

    if ( wiringPiSetup() == -1 )
        exit( 1 );

    while ( 1 )
    {
        read_dht_data();
        delay( 2000 ); /* wait 2 seconds before next read */
    }
    return(0);
}

4.Compile program using next command:

gcc -pthread -odht dht22.c -L/usr/local/lib -lwiringPi

5.Run program using next command:
./dht